## Slide 1
2D Hydrodynamics
and Water Quality Model
CE-QUAL-W2
August 12, 2021

## Slide 2: Types of Models
Completely mixed (0-order)
One dimensional (1-D)
  Usually longitudinal
Two dimensional (2-D)
  Longitudinal and vertical
Three dimensional (3-D)
More
data
Completely mixed
reactor
Deep, vertically
segmented
River-run impoundment,
longitudinally & vertically
segmented
Elongated, shallow,
longitudinally
segmented

## Slide 3: Types of Models
Zero dimensional (0D) models
  RECOVERY sediment and contaminant model
One dimensional (1D) models
  HEC-RAS hydraulics, sediment and water quality model
Two dimensional (2D) models
  CE-QUAL-W2 hydrodynamic and water quality model
Three dimensional (3D) models

## Slide 4: Factors in Model Choice
Development of conceptual model
Consideration of processes that can and cannot be modeled
Selection of appropriate level of analysis (i.e., model type)
Assurance of adequate replication of in-situ processes known to be important
Trade-offs between model complexity and cost (data needs, expertise, computational cost)
  What is the level of existing data?
  What levels of resources/technical expertise exist?
  Does model provide adequate level for decision making?

## Slide 5: CE-QUAL-W2
Laterally-averaged longitudinal/vertical hydrodynamics and water quality model
Applicable to sloping rivers, lakes, reservoirs, and estuaries and any combination thereof
Able to model multiple water bodies and branches
Able to model any number of general constituents, inorganic suspended solids, algal, periphyton, zooplankton, and CBOD groups, and their impacts on algal/ nutrient/dissolved oxygen interactions
Used in 400 systems throughout the U.S. and the world for reservoir operations and thermal and water quality studies
Open Source
http://www.cee.pdx.edu/w2/

## Slide 6: CE-QUAL-W2
Qout
z
x
w
u
g
z
x
a
Slope=S=tana
w
u
River Section
Reservoir Section
(Courtesy of W2)

## Slide 7: CE-QUAL-W2 Hydrodynamics
Water surface elevations
Horizontal/vertical velocities
Temperature/density/ice cover routines
Vertical eddy viscosities/diffusivities
Flow/head boundaries
Downstream selective withdrawal
Pipes, pumps, spillways, gates, internal/external weirs, pump-storage
Dynamic shading

## Slide 8: CE-QUAL-W2 Hydraulic Structures

## Slide 9: CE-QUAL-W2 Hydrodynamics
Continuity Equation:
x-Momentum Equation:
z-Momentum Equation:
Laterally averaging

## Slide 10: CE-QUAL-W2 Water Quality
# Arbitrary Constituents
# Inorganic suspended solids groups
CH4, H2S
N2, DGP, TDG
# labile and refractory dissolved organic matter groups (DOM, DOC, DON, DOP)
# labile and refractory particulate organic matter fractions (POM, POC, PON, POP)
Dissolved and particulate silica

## Slide 11: CE-QUAL-W2 Water Quality
Alkalinity, Total inorganic carbon (TIC), PH
# different algal groups
NH4-N, NO3-N+NO2-N
PO4-P
Fe, Mn
# CBOD groups
Sediment diagenesis model
SYSTDG

## Slide 13: CE-QUAL-W2 Water Quality
Laterally averaging
Kinetics

## Slide 14: CE-QUAL-W2 DOM

## Slide 15: CE-QUAL-W2 POM

## Slide 16: CE-QUAL-W2 Ammonium

## Slide 17: CE-QUAL-W2 Nitrate/Nitrite

## Slide 18: CE-QUAL-W2 Phosphate

## Slide 19: CE-QUAL-W2 DO

## Slide 20: CE-QUAL-W2 Algae

## Slide 21: CE-QUAL-W2 Algae

## Slide 22: CE-QUAL-W2 Bed Sediment – First Order Approach

## Slide 23: CE-QUAL-W2 Bed Sediment – Sediment Diagenesis Model

## Slide 24: CE-QUAL-W2 SYSTDG
Estimates of forebay and tailwater TDG pressures resulting from reservoir operations.

## Slide 25: Columbia River System Operations (CRSO)
Evaluate impact of operation and configuration of federal dams on
  Water temperature
  Total dissolved gases (TDG)
Develop a comprehensive Environmental Impact Statement (EIS)
Courtesy of CRSO

## Slide 26: Columbia River System Operations (CRSO)
CE-QUAL W2, 2-D modeling
HEC-RAS, 1-D modeling
model connections
Canadian System
Albeni Falls
Libby
Grand Coulee
Dworshak
Hungry
Horse
Lower
Granite
Little
Goose
Lower
Mon.
Ice
Harbor
McNary
John Day
The Dalles
Bonneville
Snake River Anatone
Rock Island
Clearwater River
Orofino
Columbia River
Int’l Boundary
Chief Joseph
Wanapum
Priest Rapids
Rocky Reach
Hanford Reach
Columbia River
Washougal
Federal dam
Non-Federal dam
Boundary condition gage
Courtesy of Dan Turner

## Slide 27: Columbia River System Operations (CRSO)
Bonneville Dam

## Slide 28: Mainstem Missouri River Reservoirs
  Fort Peck Dam (5th)
  Garrison Dam (3rd)
  Oahe Dam (4th)
  Big Bend Dam
  Fort Randall Dam
  Gavin’s Point Dam
Water quality constituents
  Temperature
  Turbidity
  Dissolved oxygen

## Slide 29: Lower Minnesota River

## Slide 30: Lower Minnesota River